## Slide 1: ECE231 Basics
Maj Kevin Walchko

## Slide 2: Equivalent Circuits
Series (all see the same current)
Parallel (all see the same voltage drop)
Given the following circuit, there are multiple nodes and loops which need to be calculated to determine the current flow through the circuit. However, we can simplify this with the idea of equivalent resistors.
(this only applies to 2 resistors)

## Slide 3: Example
Series: Eq1 = R2 & R3
Parallel: Eq2 = R5 & Eq1
Series: Eq3 = R4 & Eq2
Parallel: Eq4 = R1 & Eq3
Series: R0 & Eq4
Redraw

## Slide 4: Parallel or Series?

## Slide 5: Equivalent Resistance
I = V/R
I = 10 V / 10 kΩ
I = 1 mA
P = IV
P = 1 mA * 10 V
P = 10 mW
I = V / R
I = 10 V / ( 10 kΩ + 10 kΩ)
I = 0.5 mA
P = 0.5 mA * 10 V = 5 mW
For #2 , the added resistor increased the difficulty for current to flow through the circuit loop, thus increasing the resistance proportionally. Higher resistance means less current and lower power consumption.
1. Original
2. Series
3. Parallel
I = V / Req
I = 10 V / (100/(10 + 10) kΩ)
I = 10 V / 5 kΩ
I = 2 mA
P = 2 mA * 10 V = 20 mW
For #3, notice the Req is less than the smallest R value. Thus, less resistance means more current flow and power consumption.

## Slide 6: Current/Voltage Division
What is the voltage drop across R2?
V2 = 10 kΩ / 20 kΩ * 10 V
V2 = 5 V
Voltage Division (series)
Current Division (parallel)
What is the current across R2?
I2 = 10 kΩ / 20 kΩ * 2 mA
I2 = 1 mA
R1
R2
R1
R2
This equation is possible because all resistors in series see the same current, thus, V2/R2 = Vs/Req = Vs/Rsum
This equation is possible because all resistors in parallel see the same voltage drop, thus,
I2*R2 = Is*Req -> I2= Req/R2*Is = R1/Rsum*Is
Note: The R2 cancel

## Slide 7: Backups