## Slide 1: ECE231 Op Amps
Maj Kevin Walchko

## Slide 2: Op Amp
+
-
Inverting input (vp)
Non-inverting input (vn)
output
A
Op Amp is an active device
Theoretically the gain (A) is ∞, but typically 20k – 200k
Current in is 0
Input impedance (Zin) is ∞
Output impedance (Zout) is 0
No voltage difference between vp and vn
and
Vcc = power source
Linear mode:
Saturation mode:
or
A = open loop gain
K = closed loop gain

## Slide 3: Ideal Op Amp
We will always assume an ideal op amp
VCVS, in open loop, there is a small difference between vp and vn

## Slide 4: Non-inverting Op Amp
Find Vout and gain (K)

## Slide 5: Inverting
Find Vout and gain (K)

## Slide 6: Simple Examples
If a non-inverting op amp circuit is operating with R1 = 2R2 and Vcc = ± 12V, what is the gain?
Design an inverting op amp with a gain of 30 ± 10% (use standard resistor values)
A 2mV signal needs to be amplified by a gain of k = -450 ± 10%. Design an amp to do this.
Find Vout of an inverting amp with R1 = 10kΩ, R2 = 33kΩ, Vcc = ± 15V when Vin is 2V, 4V, and 6V.

## Slide 7: Backups