## Slide 1: ECE231 Op Amps III
Maj Kevin Walchko

## Slide 2: Example from last time
Design a circuit that implements:
  Vout = 8V2 – 2 V1 (use a differential amp)
  and

## Slide 3: Summary
K
Vin
Vout=KVin
Non-inverting Op Amp
-K
Vin
Vout=-KVin
Inverting Op Amp
-K1
-K2
-Kn
Vin1
Vin2
Vinn
+
Vout=-K1*Vin1-K2*Vin2-…-Kn*Vinn
Summing Op Amp
K1
-K2
Vin1
Vin2
+
Vout=K1*Vin1-K2*Vin2
Differential Op Amp
…
1
Vin
Vout=Vin
Buffer
More than one way to draw these, Fig 4-48, pg 188 is different

## Slide 4: Implement the following
Vout = 6V1-18V2+3
Use 2, 2 input summers:
-6
-1
Vin1
Vin2
+
Vstage1=-6*Vin1-1*3
+
3V
-18
-1
Vout=6*Vin1+3-18*Vin2
Use an inverter and a summer w/ 3 inputs:
-1
-1
Vin1
+
-3V
-18
-6
Vin2
Vout=6*Vin1+3-18*Vin2
Vstage1=-6*Vin1

## Slide 5: Loading with Thevenin Sources
Inverting:
w/ Thevenin source:
Op Amp | Loading Issues
Non-inverting | No
Inverting | Yes
Summer | Yes
Differential | Yes
Buffer | No
Vin is not the voltage across R1
This is where buffering comes in, no current flow across RT, thus VT is what the op amp sees

## Slide 6: Implement this equation
Vout=-50*Vin1-20*Vin2+5
What is the equation?
V1
V2
1
Vout

## Slide 7: Can We Do Better?
V1
V2
V3
Vout

## Slide 8: Backups

## Slide 9: Summer

## Slide 10: Differential Amp (Subtractor)

## Slide 11: Examples
Design an inverting summer that implements:
  Vout = -(5VA + 13VB)
Using the above gains, find Vout if VA = 2V and VB = -.5V
Using the above and VA = 500 mV, Vcc = 15V, what is the maximum value of VB and still have it be linear?
Design a circuit that implements:
  Vout = 8V2 – 4 V1 (use a differential amp)

## Slide 12: Find Vout
VB
+
-
Non-inverting
Inverting

## Slide 13: Buffer
Short
Open
circuit
Vout
+
-
Vout
+
-
Looking at the non-inverting op amp
Buffers help circuits with different impedances work correctly without overloading one another or effecting operation

## Slide 14: Example
(a) Find the transfer characteristics of a differential amplifier if:
R1 = 10k Ω
R2 = 40k Ω
R3 = 10k Ω
R4 = 15k Ω
(b) If Vcc is ± 15 V and V1 = 3V, what is the allowable range of V2 for linear ops?
Vo = -4V1 + 3V2
-1 V ≤ V2 ≤ 9 V