## Slide 1: ECE231 Basics
Maj Kevin Walchko

## Slide 2: Electric Charge & Voltage
Voltage is the difference in charge between two points.
Current is the rate at which charge is flowing.
Resistance is a material’s tendency to resist the flow of charge (current)
Ohms Law: v=iR
Power:

## Slide 3: Electricity … the lie!
Battery
+
-
Circuit
e-
e-
e-
e-
e-
1827: Ohms Law
1897: Electron discovered
+
-
repel
+
-
repel
attract
+
-
Passive Sign Convention: we are going to say current flows from positive to negative

## Slide 4: Some Common Circuit Symbols
https://xkcd.com/730/
Loads
Sources/Sinks
+
-

## Slide 5: Simple DC Circuit
Electrons (negative) really flow from (-) to (+), but due to convention (Ben Franklin) we say current (positive) flows from (+) to (-).
What is the LED power consumption?
P = IV or P = I(IR) = I2R
P = (0.018 A)(9V) P = (0.018)*(0.018)*(500Ω)
P = 0.162 W P = 0.162 W
P = 162 mW
What is the resistor value if I = 18 mA?
(+) hot
(-) ground

## Slide 6: Kirchhoff's Current Law (KCL)
The principle of conservation of electric charge implies:
At any node (junction) in an electrical circuit, the sum of currents flowing into that node is equal to the sum of currents flowing out of that node
#1
#3
#2
#4
How many nodes below?
When you cut out the components, everything left is a node
The current entering any junction is equal to the current leaving that junction. i2 + i3 = i1 + i4

## Slide 7: How Many Nodes?
4
6
6
4
1.
2.
3.
4.

## Slide 8: KCL Eqns
#1
#3
#2
#4
+
-
+
+
+
-
-
-
#1
iv1
iR1
iR4
#2
iR2
iR1
iR3
#3
iv2
iR3
iR4
#4
iv2
iR2
iv1
Remember, we define current flows from positive (+) to negative (-)
#1: iv1+iR4= iR1
#2: iR1+iR3= iR2
#3: 0= iR4+iR3+iv2
#4: iv2+iR2= iv1
Write eqns: current out = current in
We typically reverse the direction for voltage sources

## Slide 9: Kirchhoff's Voltage Law (KVL)
The principle of conservation of energy implies that
The directed sum of the electrical potential differences (voltage) around any closed network is zero.
The sum of all the voltages around a mesh is equal to zero.
v1 + v2 + v3 - v4 = 0
Can use these equations and Ohms Law (V=IR) to solve help solve for other things.
Mesh 1: -B1 + R1 + R2 = 0
Mesh 2: R2 + R3 – B2 = 0

## Slide 10: How Many Meshes?
2
3
3
3
1.
2.
3.
4.

## Slide 11: Simple Example
KCL:
N1: Is = I1
N2: I1 = I2 + I3
N3: I2 + I3= Is
N2
N1
N3
Vs
KVL:
Mesh A: VS - V1-V2 = 0
5V - I1 ∗ 1000 Ω - I2 ∗ 1000 Ω = 0
5V = I1 ∗ 1000 Ω + I2 ∗ 1000 Ω
Mesh B: V2 – V3 = 0
I2∗1000 Ω – I3∗1000 Ω = 0
+
-
+
-
+
-
A
B
2 eqns, 3 unknowns …??
3 eqns, 3 unknowns … we can solve
We will fix this when we do mesh analysis

## Slide 12: Backups

## Slide 13: Simple Example
KCL:
J1: Is = I1 J2: I1 = I2 + I3 J3: I2 + I3= Is
2
1
3
Vs
KVL:
Mesh A: VS - V1-V2 = 0
5V - I1 ∗ 1000 Ω - I2 ∗ 1000 Ω = 0
5V = I1 ∗ 1000 Ω + I2 ∗ 1000 Ω
Mesh B: V2 – V3 = 0
I2∗1000 Ω – I3∗1000 Ω = 0
Put into terms for 2 & 3:
5V = I1 ∗ 1000 Ω + I2 ∗ 1000 Ω
5V = (I2 + I3) ∗ 1000 Ω + I2 ∗ 1000 Ω
5V = I2 ∗ 2000 Ω + I3 ∗ 1000 Ω
Add Eqns:
5V = I2 ∗ 2000 Ω + I3 ∗ 1000 Ω
0 = I2∗1000 Ω – I3∗1000 Ω
5V = I2 ∗ 3000 Ω
I2 = 1.67 mA
I3 = I2 = 1.67 mA
Is = 3.33 mA
+
-
+
-
+
-
A
B