## Slide 1: ECE231 Basics
Maj Kevin Walchko

## Slide 2: To Pass this class you must know:
Current division
Voltage division
Nodal analysis
Mesh analysis
Superposition
Thevenin analysis
We’ll talk about this today

## Slide 3: Equivalent Circuits
Series (all see the same current)
a node is connect to 1
component
Parallel (all see the same voltage drop)
a node is connected to multiple
components
Given the following circuit, there are multiple nodes and meshes which need to be calculated to determine the current flow through the circuit. However, we can simplify this with the idea of equivalent resistors.
(this only applies to 2 resistors)

## Slide 4: Which Resistors are in Parallel or Series?

## Slide 5: Example
Series: Eq1 = R2 & R3
Parallel: Eq2 = R5 & Eq1
Series: Eq3 = R4 & Eq2
Parallel: Eq4 = R1 & Eq3
Series: R0 & Eq4
Redraw

## Slide 6: Equivalent Resistance
I = V/R
I = 10 V / 10 kΩ
I = 1 mA
P = IV
P = 1 mA * 10 V
P = 10 mW
I = V / R
I = 10 V / ( 10 kΩ + 10 kΩ)
I = 0.5 mA
P = 0.5 mA * 10 V = 5 mW
For #2 , the added resistor increased the difficulty for current to flow through the circuit loop, thus increasing the resistance proportionally. Higher resistance means less current and lower power consumption.
1. Original
2. Series
3. Parallel
I = V / Req
I = 10 V / (100/(10 + 10) kΩ)
I = 10 V / 5 kΩ
I = 2 mA
P = 2 mA * 10 V = 20 mW
For #3, notice the Req is less than the smallest R value. Thus, less resistance means more current flow and power consumption.
Weapon systems tend to connect payloads in parallel … why?

## Slide 7: Current/Voltage Division
What is the voltage drop across R2?
V2 = 10 kΩ / 20 kΩ * 10 V
V2 = 5 V
Voltage Division (series)
Current Division (parallel)
What is the current across R2?
I2 = 10 kΩ / 20 kΩ * 2 mA
I2 = 1 mA
R1
R2
R1
R2
This equation is possible because all resistors in series see the same current, thus, V2/R2 = Vs/Req = Vs/Rsum
This equation is possible because all resistors in parallel see the same voltage drop, thus,
I2*R2 = Is*Req -> I2= Req/R2*Is = R1/Rsum*Is
Note: The R2 cancel

## Slide 8: KVL
A
C
B
D
E
F
Voltage rise and drops are 0 around a mesh
1
2
3
+
-
+
-
+
-
+
-
+
-
+
-
15V
5V
10V

## Slide 9: Backups