## Slide 1: ECE231 Voltage/Current Division
Maj Kevin Walchko

## Slide 2: Review Kirchhoff's Laws
KCL
  at nodes
  Conservation of electric charge
KVL
  Meshes contain no other loops/meshes inside
  Conservation of energy

## Slide 3: Review Equivalent Circuits
Series (all see the same current)
Parallel (all see the same voltage drop)
Given the following circuit, there are multiple nodes and loops which need to be calculated to determine the current flow through the circuit. However, we can simplify this with the idea of equivalent resistors.
(this only applies to 2 resistors)

## Slide 4: Problems
(a)
(b)
(c)
Power provide by source?
Voltage drop across 2Ω and 7Ω?
Power produced by source?
Current across 10Ω?
Voltage drop across resistors?
Current across one resistor?

## Slide 5: Mesh Example
Find Vx using KVL
Vx
+
-
You can also do this via voltage divider too

## Slide 6: KCL
P
R
S
4V
Q
10V
-2A
1A
A
B
C
Find the missing currents using KCL and what are the power consumptions of each component?
Hint:
+
-
What might this component be?
+Pwr – consume
-Pwr – provide

## Slide 7: House
R7
100
R8
100
Ω
Find the resistance measured by the ohmmeter
Hint: find your nodes, what’s in serial or parallel?

## Slide 8: Backups

## Slide 9: Example
Series: Eq1 = R2 & R3
Parallel: Eq2 = R5 & Eq1
Series: Eq3 = R4 & Eq2
Parallel: Eq4 = R1 & Eq3
Series: R0 & Eq4
Redraw

## Slide 10: Parallel or Series?

## Slide 11: Equivalent Resistance
I = V/R
I = 10 V / 10 kΩ
I = 1 mA
P = IV
P = 1 mA * 10 V
P = 10 mW
I = V / R
I = 10 V / ( 10 kΩ + 10 kΩ)
I = 0.5 mA
P = 0.5 mA * 10 V = 5 mW
For #2 , the added resistor increased the difficulty for current to flow through the circuit loop, thus increasing the resistance proportionally. Higher resistance means less current and lower power consumption.
1. Original
2. Series
3. Parallel
I = V / Req
I = 10 V / (100/(10 + 10) kΩ)
I = 10 V / 5 kΩ
I = 2 mA
P = 2 mA * 10 V = 20 mW
For #3, notice the Req is less than the smallest R value. Thus, less resistance means more current flow and power consumption.

## Slide 12: Current/Voltage Division
What is the voltage drop across R2?
V2 = 10 kΩ / 20 kΩ * 10 V
V2 = 5 V
Voltage Division (series)
Current Division (parallel)
What is the current across R2?
I2 = 10 kΩ / 20 kΩ * 2 mA
I2 = 1 mA
R1
R2
R1
R2
This equation is possible because all resistors in series see the same current, thus, V2/R2 = Vs/Req = Vs/Rsum
This equation is possible because all resistors in parallel see the same voltage drop, thus,
I2*R2 = Is*Req -> I2= Req/R2*Is = R1/Rsum*Is
Note: The R2 cancel

## Slide 13: KCL
P
R
S
4V
Q
10V
-2A
1A
A
B
C
Write the node equations for the circuit below and find the missing currents
Hint: sum current in = sum current out